## Slide 1: Heat transfer correlations for BIPV/T systems
Luis Candanedo
Concordia University
Montreal, November 23th, 2009

## Slide 2: Overview
Introduction
Complexity
Numerical modeling
Experimental setup - Smooth cavity
Data Reduction / Correlations
Grashof number
Comparison with previous correlations
Papers (Journal Publications (ASHRAE&ASME)
In development: framing effects and tilt angle

## Slide 3: Introduction
Literature review showed that typical correlations for pipes and ducts underestimated the convective heat transfer coefficients in BIPV/T systems (Eicker et al, 1999, Bazilian and Prasad 2002, Bloem, 2004 and Charron and Athienitis 2006)
Experimental measurement of convective heat transfer coefficients has been carried out @ Concordia using a BIPV/T channel setup. The approach consists to study first a smooth configuration and then framing effects to have Nusselt number limits.

## Slide 4: Intro… cont
Researchers recommend to use a combination of natural convection Nusselt number correlation (or laminar flow) with forced flow correlations. (See details in Paper)
E.g. Eicker, 2003 recommends for a ventilated PV vertical façade
.

## Slide 5: Complexity
-Non uniform heat fluxes or temperatures across boundaries.
-Natural convection effects.
-Framing effects.
-Developed Vs Non developed flow conditions.

## Slide 6: Numerical Modeling
See papers SBRN conference in Toronto (Candanedo et al, 2009) and ASHRAE (Candanedo et al, 2010).

## Slide 7: Experimental Setups
Amorphous PV module 6% ηe

## Slide 8: Ecoterra House

## Slide 9: Measured variables
Temperature distributions along PV interior surface and insulation.
Temperature rise of the air.
Accurate measurement of the airflow inside the channel (CFM).
Surfaces long-wave emissivities.
Electrical power output.
Ambient air temperature and inlet air temperature, relative humidity and exterior wind speed.

## Slide 10: Features
No thermal gradients across the width were observed.
Major emphasis of temperature variation along the length.
Negligible heat loss through the bottom surface (combined R ≈ 1.96 RSI
Aspect ratio, Width/Height of 10 in order to represent a roof BIPV/T installation.
Length/Hydraulic Diameter of 38.
Tilt angles tested (45 & 30 degrees from horizontal)

## Slide 11: Data Reduction
Non dimensional numbers employed, Nusselt & Reynolds numbers, x/Dh, Grashoft numbers
Dh = 4Ac/U, where U is the wetted perimeter

## Slide 12
Eliminating transient effects.
Due to thermal mass of PV modules
and air flow rate.

## Slide 13: Air temperature distribution inside the channel (Time Response)

## Slide 14: Air Temperature distribution
where A, B, and C are fitted parameters. The correlation coefficients (R2) of the regressions shown in Figure 6 are high (R2≈ 0.99).

## Slide 15: Computation of CHTC’s
Since there is negligble heat loss through the bottom surface, it follows that:

## Slide 16: Nusselt numbers

## Slide 17: Nusselt number distribution

## Slide 18
Nusselt number at the PV surface

## Slide 19: Nusselt number at the bottom surface

## Slide 20: Comparison with other correlations

## Slide 21: Grashof number

## Slide 22
Most of the experimental data falls in the mixed regime of turbulent heat transfer (2×1010<Ra<5×1010).
The experimental data is also in agreement with the results obtained by Sudo et al. [51]

## Slide 23: Papers
Candanedo, L.M., A.K. Athienitis, J. Candanedo, W. O'Brien, and Y.-X. Chen, Transient and steady state models for open-loop air-based BIPV/T systems. ASHRAE transactions, 2010. (accepted)
Candanedo, L.M, A.K. Athienitis. Convective Heat Transfer Coefficients in a Building-Integrated Photovoltaic/Thermal System. Submitted to ASME Journal of Solar Energy Engineering, October 14th, 2009.

## Slide 24: New Correlations under development
Correlations at 30 degree tilt angle (Top and bottom surfaces)
Results show a negligible reduction of Nusselt number due to the tilt angle.
Correlation including wood framing effects. Soon to be finished. This week. Results show increased Nusselt number by around 30% compared to the 45 degree tilt angle correlation .

## Slide 25: Questions / Comments Thank you