## Slide 1: SBRN Sub-Project 4.2 a/b a – Comprehensive modelling of the energy end-uses and GHG emissions of the Canadian housing stock B – Assessing the impact of solar technologies and integration strategies
Lukas Swan – Dalhousie Univ.

## Slide 2: CHREM Model
CSDDRD (17,000 houses)
Neural Network
ESP-r
GHG emission factors

## Slide 3: CHREM Status
Complete
  Database
  NN
  Integration of A&L and DHW into ESP-r
  Generation of houses into ESP-r models
    Recent effort was multilayer constructions
  GHG factors (Amal Farhat, 2009)

## Slide 4: CHREM Status
Incomplete
  Final results collation
  Verification (have acquired data)
  Demonstrate solar technology

## Slide 5: CHREM Intent
Detailed model
  Simulating solar technologies
  Capture variety of housing stock
Technology models enter through ESP-r
Unfortunately, few technologies added
  CFC
  BIPV/T with HP
  Phase change?

## Slide 6: CHREM and ESP-r
ESP-r requires a house model (set of files)
CHREM generates the files using Perl
  Configuration – climate
  AIM2 - infiltration
  Mechanical ventilation
  Control
  HVAC
  DHW
  Obstructions and shading (Sara)

## Slide 7: CHREM and ESP-r
CHREM generates the files using Perl
  Determine zones (bsmt, crawl, main(s), attic/roof)
    2 to 5 zones

## Slide 8: CHREM and ESP-r
CHREM generates the files using Perl
  Geometry
    Rectangular
    Independent zone size (exterior)
    Windows & frames
    Doors
  Construction and connections
    Determine facing condition
    Build layer by layer from code (e.g. 11A59G4L)
      Siding, sheathing, insulation_2, insulation_1 (modified), interior

## Slide 9: CHREM and ESP-r
CHREM generates the files using Perl
  Operations
    Occupants
    Fixed air flows
      Infiltration (attic/roof or crawl space)
      Zone to Zone
  BCD file
    Links Stove, Dryer, AL-Other (heat or not?)
    Select appropriate profile
  Electrical Network
    1 – AC node
    Power only loads

## Slide 10: How to implement new technology into CHREM?
Your expertise
  Understand the technology
  Simplification for modeling
  Example in ESP-r
  Determine sizing calculations
  What makes a house applicable
Alouette Homes, 2007

## Slide 11: How to implement new technology into CHREM?
Our expertise
  Use characteristics (data) to determine applicable houses
  Make templates for technology changes
  Size system (calculation)
  Generate the ESP-r model file
  Simulate

## Slide 12: Potential Difficulties
We are multi-zone for main levels
  Inject based on volumetric proportion?
  Inject in one zone and use zone-zone ventilation?
Roof area – perhaps very different from level 1

## Slide 13: Key questions
Do you have a:
  Change in ESP-r source code to facilitate?
  Working ESP-r example?
  Application determination method?
  Sizing methodology using available characteristics?
This is what I hope to learn here about the BIPV/T